## Slide 1: Participatory Modeling of Complex Urban Infrastructure Systems (Model Urban SysTems, MUST)
John C. Crittenden, Ph.D., P.E., NAE (US & China)
Zhongming Lu, Ph.D.
Brook Byers Institute for Sustainable Systems,
Georgia Institute of Technology, Atlanta, GA
E-Mail: john.crittenden@ce.gatech.edu

## Slide 2
Conference website:
http://www.icsi2016.org/

## Slide 3: Introduction of MUST
Food
Systems dynamics modeling of complex urban infrastructure systems (i.e., the Metamodel).
Quantifying the resilience of urban infrastructure systems.
Social, Behavioral, and Economic decision making.
Optimizing between resilience and sustainability.
Research Elements:

## Slide 4: MUST Investigators
Name | Affiliation
Ashuri, Baabak | Associate Professor, School of Building Construction; Director, Economics of the Sustainable Built Environment (ESBE) Lab
Bras, Bert | Professor, George W. Woodruff School of Mechanical Engineering.
Clark, Jennifer | Associate Professor in the School of Public Policy and Director of the Center for Urban Innovation in the Ivan Allen College
Crittenden, John | Director, Brook Byers Institute for Sustainable Systems, Hightower Chair and Georgia Research Alliance Eminent Scholar in Environmental Technologies; School of Civil and Environmental Engineering
Fujimoto, Richard | Regents’ Professor in the School of Computational Science and Engineering
Grijalva, Santiago | Associate Professor; Associate Director for Electricity Strategic Energy Institute (SEI); Georgia Power Distinguished Professor
Guhathakurta, Subhrajit | Professor, School of City and Regional Planning; Director, Center for Geographic Information Systems
Leigh, Nancey Green | Associate Dean For Research, College of Architecture; Professor, School of City and Regional Planning;
McDermott, Tom | ‎Director of Technology Policy Research, Georgia Tech Research Institute
Thomas, Valerie | Anderson Interface Professor of Natural Systems, School of Industrial and Systems Engineering
Weissburg, Marc | Professor, School of Biology

## Slide 5: MUST Investigators: Expertise
Name | Expertise / Role in Project
Ashuri, Baabak | Infrastructure Project Finance & Investment Science, Systems Engineering, Infrastructure project development processes & delivery systems, Risk Management, & Operations Research (Business Analytics & Data Mining)
Bras, Bert | Computer-aided engineering, design and manufacturing; environmentally conscious design, design for recycling and robust design
Clark, Jennifer | Regional economic development, manufacturing, industry clusters and innovation
Crittenden, John | Sustainable systems, pollution prevention
Fujimoto, Richard | Execution of discrete-event simulation programs on parallel and distributed computing platforms
Grijalva, Santiago | Power system and smart grid computation; De-centralized and autonomous power control architectures; Ultra-reliable electricity internetworks; Seamless integration of large-scale renewable energy; Electricity markets design and power system economics
Guhathakurta, Subhrajit | Geographic information systems, planning support systems, sustainability
Leigh, Nancey Green | Economic development planning, sustainable development, urban andregional theory, industrial restructuring, income inequality
McDermott, Tom | Modeling dynamic systems, systems thinking, organizational and team behavior, management of technology
Thomas, Valerie | Energy and materials efficiency, sustainability, industrial ecology, technology assessment, international security, science and technology policy
Weissburg, Marc | Ecology, community ecology, biologically Inspired design methodology and pedagogy

## Slide 6
Water Supply
Waste water Treatment & Discharge
Energy for Water
Carbon Emissions
Water
Fresh Surface
Fresh Ground
Saline Surface
Rain
Water
Energy
Water for Energy
Energy for Water
Oil
Biomass
Natural Gas
Coal
Geothermal
Hydro
Wind/Solar
Land Use
Fuel
Electricity
Transport
Residential
Commercial
Industrial
Agriculture
Water Evaporation
Water
Energy
Carbon
Interdependences of Urban Infrastructure Systems

## Slide 7: Defining Infrastructure Ecology
Infrastructure Ecology is an emerging transdiscipline:
  Infrastructure Ecology alters and reorganizes energy and resource flows and considers the potential synergistic effects arising from infrastructure symbiosis.
“Understanding the city as an ecosystem requires knowledge of how human and natural infrastructure systems interact to create emergent properties.”
These “infrastructures” include physical infrastructure systems and their interactions (e.g., water-transportation−energy nexus), as well as ecological infrastructure, information and communications technology (ICT) infrastructure, socio-economic infrastructure (e.g., banking, finance) and social network infrastructure.”
It is Transdisciplinary. - It creates a body of knowledge distinct from its antecedents (engineering, ecology) that fundamentally changes the questions that are asked, and the tools used to answer them.
Developing a Science of Infrastructure Ecology for Sustainable Urban Systems
Ming Xu, Marc Weissburg, Joshua P. Newell, and John C. Crittenden
(2012, 46 (15), pp 7928–7929)

## Slide 8: Infrastructure Symbiosis: System-based Design Recognizing the Interdependence

## Slide 9: Water Resource Withdrawal Profile in the United States
Chart: 
| Public Supply | Industrial | Thermoelectric | Irrigation | Aquaculture | Livestock | Domestic | Mining
 | 0.13 | 0.05 | 0.39 | 0.4 | 0.01 | 0.01 | 0.01 | 0.01
Decentralized
Energy Production
Urban Farming

## Slide 10: Low Impact Development (Reducing Storm Water Runoff, Erosion and Surface Water Contamination) - LID Best Management Practices (BMPs)

## Slide 11: Typical Greywater Reclamation System at the Household Level
Source: http://www.environmentwriter.com/wp-content/uploads/greywater1.jpg
Note: N.S.W. denotes New South Wales, Australia

## Slide 12: Water Flows with LID and Reclamation a 2-story apartment unit of Atlanta, GA
Same Size Waste Water Treatment Plant
Smaller Flow, More Concentrated; Smaller Plant: Better energy and nutrient recovery.
Smaller Water Treatment Plant
Potential of off-grid water supply

## Slide 13: Decentralized Energy Production at Perkins + Will, Atlanta Office
Microturbines are used to for heating and cooling using Absorption Chillers and supply 40% of the total electricity.
Adsorption Chiller
65 kW Microturbine
Perkins+Will Office Building
Water Reduction: >50%
CO2 Reduction: 15 - 40%
NOX Reduction: ~90%
Adding Distributed Generation as part of the Grid:

## Slide 14: Future Research: Expanding the Current CCHP System 2.0
Wind

## Slide 15: Dispatch Optimization of Electric Energy Output Minimize the Generation Cost and Maximize the Environmental Benefits
Electric Energy from Grid (No MT and No PV)
Electric Energy from Grid, MT, and PV
Cooling load (up to 80.7 kW) is covered by chillers of MT
Peak reduction by PV and MT
 | Office Size | Small
Office | Number of Floors | 1
 | Floor Area in ft2 | 5,500
 | Electric and Thermal Peaks | 19.4 kW (July/07)
 | Number of Buildings | 22
MT | Number of 65-kW Capstone MTs | 1
 | Penetration % of MT from Peak [4-5] | 
PV | Total Capacity [4-5] | 65 kW
 | Penetration % of PV from Peak | 
 | PV Location and Lifetime | Atlanta (Facing South) and 30 Years
 | Office Size | Small
Office | Number of Floors | 1
 | Floor Area in ft2 | 5,500
 | Electric and Thermal Peaks | 19.4 kW (July/07)
 | Number of Buildings | 22
MT | Number of 65-kW Capstone MTs | 1
 | Penetration % of MT from Peak [4-5] | 
PV | Total Capacity [4-5] | 65 kW
 | Penetration % of PV from Peak | 
 | PV Location and Lifetime | Atlanta (Facing South) and 30 Years
Credit: Insu Kim

## Slide 16: Closing the Urban Water, Nutrient, Energy and Carbon Loops
Urban Agriculture (Aquaponics,
Urban Farming, Greenhouse Farm)
Stormwater Management with Low-Impact Development
More Concentrated Wastewater
On-site Energy and Nutrient Recovery
Source of Fertilizer
Harvested Rainwater
Stormwater treated through LID
Combined Carbon Capture, Cooling, Heating and Power (Air-cooled microturbines)
Heat and Energy
Local Composting
Fertilizer for Farms,
Food for Aquaponics
Heat
Natural Gas from Anaerobic Digestion
Natural Gas from Compost
Natural Gas
Heat and Energy
Water
Fertilizer
Natural Gas
CO2 Injection
CO2
Landfill
Natural Gas from Landfill

## Slide 17: The Design of Decentralized Water, Energy and Food Systems in Rural Baoting, Hainan
One single family with 5 people | Conventional | Decentralized | Change
Land use (including housing and farming) | More than 400 m2 | Less than 100 m2 | -75%
Water use | More than 200 tones/year | Less than 120 tones/year | -40%
Chemical fertilizer use | More than 40 kg/acre/year | Less than 10 kg/acre/year | -75%
Pesticide use | More than 1kg/acre/year | Less than 0.1 kg/acre/year | -90%
Net household income | Less than ￥40,000/year | More than ￥50,000/year | +20%
Credit: Baolong Han, RCEES
The installation cost: ￥50,000 ($8,000)

## Slide 18: The Connection between Autonomous Vehicles and Water
80% penetration of autonomous vehicles
28% of the cars we have today
At least 72% reduction in parking space
Additional 17% of city land for green space and stormwater management
24.7% reduction of impervious area and stormwater runoff
Notes: https://www.itreetools.org/Canopy/resources/Tree_and_Impervious_Cover_change_in_US_Cities_Nowak_Greenfield.pdf

## Slide 19: The Adoption of Shared Autonomous Vehicles Might Boost the Return on Investment of Transit-oriented Development
¾ mile or 10 minute walking
¾ mile or 10 minute walking
¾ mile or 10 minute walking
¾ mile or 10 minute walking
The radius served by transit can be extended through the enhanced mobility with autonomous vehicles.

## Slide 20: The Synergistic Effects of “Infrastructural Symbiosis”
The accumulated synergistic effects :
  reduced water and energy consumption,
  lower dependence on centralized systems,
  larger share of renewables in the electricity mix,
  reduced vehicle-miles travelled, &
  an increase in tax revenue.
  enhanced system resilience
Low-Impact Development
Greywater Reclamation
Rainwater Harvesting
Air-cooled Microturbine
Residential PV, Wind, etc
Vehicle-to-Grid (V2G)
Compact Growth
Preferred Neighborhood
Transit – oriented Development
Decentralized Water Infrastructure
Decentralized Energy Infrastructure
Increased
Neighborhood Amenities
Mixed Land Use
Autonomous Vehicles
Thermal and Energy Storage

## Slide 21: Manage the Complexity in Infrastructure Systems

## Slide 22: Urban Systems Complexity Emergence of desirable amenities (high Tax Revenue and Quality of Life) & undesirable amenities (e.g., poor air quality, low tax revenue, traffic congestion, flooding, etc.)
Macro
Micro
Infrastructure Systems
Socio-Economic Environment
Notes: Infrastructures (pipelines, roads, buildings) serve for human activities in the urban areas. Meanwhile, the increasing wealth and population stimulates the growth and renovation of infrastructures. In the micro level, the interconnection is determined by thousands, millions, even billions of decisions related to geo information, socioeconomic status, and willing pay. That’s what we can observe various land use pattern, water, energy and transportation network in the macro level.

## Slide 23: Big Data for Social Decision and Complexity Modeling
Topic Modeling
Collect
Social Media
Analyze
Enrich and prepare social media content with metadata
Modeling
Agent-based urban model and visualization
Blogs
Twitter
News
Product Reviews

## Slide 24: Sentiment Analysis on the Topic of “Green Roof”
We synthesized the topics of 1.2 millions sustainability-related tweets collected from April, 2016 to June, 2016. The topic modeling algorithm takes less than 40 minutes.
In 6054 tweets about “green roof” topics:
  4543 tweets are neutral
    “We do green roof systems for today’s homeowners and building owners”
  1422 tweets are positive
    “4 best reason to grow a living roof! Beautiful, beneficial, efficient, green living rooftops”
  89 tweets are negative
    “Green roof garage has been nixed. Too expensive. :(”

## Slide 25: Agent-based Housing Market Simulation
Housing Market
House inventory:
apartment, single-family
Infrastructure service
Stormwater management(1st yr)
Transportation improvement (5th yr)
Prospective homebuyers
Socioeconomic attributes
Preference
Evaluate candidate houses
Decide the biding house
Determine willingness to pay
Homeowners
Property value
Living community
Green space
Transportation accessibility
Developers
Asking price
New house investment decision
Consider LID options if impact fee exists
Apartment
vs. Single-family
Transaction price
Estate sale
Government
Collect property tax
Distribute property tax for infrastructure improvement
Bid Price
Bid Success
Asking Price
New houses
Impact fee ?
House demand for next period
Infrastructure
improvement
Property Tax

## Slide 26: Agent-based Modeling: Simulating the Adoption Rate for More Sustainable Urban Development
Chart: Year
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30
Percentage of households as compared to total households after 30 years | 0.040741 | 0.071974 | 0.10608 | 0.13866 | 0.17192 | 0.20534 | 0.23856 | 0.27175 | 0.30484 | 0.33802 | 0.37128 | 0.40452 | 0.43771 | 0.47111 | 0.50417 | 0.53735 | 0.57054 | 0.60375 | 0.63665 | 0.66984 | 0.70281 | 0.736 | 0.7692 | 0.80215 | 0.83515 | 0.86811 | 0.90116 | 0.93411 | 0.96714 | 1
Percentage of households in single-family houses as compared to total households after 30 years | 0.024336 | 0.0435 | 0.063629 | 0.085794 | 0.10724 | 0.12884 | 0.15035 | 0.17189 | 0.19347 | 0.21504 | 0.23676 | 0.25854 | 0.28007 | 0.30191 | 0.32343 | 0.3451 | 0.36678 | 0.38832 | 0.40978 | 0.4315 | 0.45317 | 0.47477 | 0.49649 | 0.518 | 0.53955 | 0.56106 | 0.5826 | 0.60416 | 0.62561 | 0.64713
Percentage of households in apartments as compared to total households after 30 years | 0.016405 | 0.028474 | 0.04245 | 0.05287 | 0.064677 | 0.076503 | 0.088211 | 0.099862 | 0.11137 | 0.12299 | 0.13451 | 0.14597 | 0.15764 | 0.1692 | 0.18074 | 0.19226 | 0.20375 | 0.21542 | 0.22687 | 0.23833 | 0.24963 | 0.26123 | 0.27271 | 0.28414 | 0.2956 | 0.30705 | 0.31856 | 0.32996 | 0.34153 | 0.35287
Chart: Year
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30
 | 0.038335 | 0.067966 | 0.10096 | 0.13395 | 0.16668 | 0.20064 | 0.2339 | 0.26734 | 0.30074 | 0.33411 | 0.36728 | 0.40077 | 0.43404 | 0.46746 | 0.50081 | 0.53402 | 0.56733 | 0.6004 | 0.63373 | 0.66721 | 0.7005 | 0.73388 | 0.76703 | 0.80037 | 0.83364 | 0.86692 | 0.90013 | 0.93352 | 0.96672 | 1
 | 0.02179 | 0.038239 | 0.055313 | 0.072903 | 0.089407 | 0.10563 | 0.12036 | 0.13446 | 0.148 | 0.16138 | 0.17469 | 0.18765 | 0.20071 | 0.21361 | 0.22632 | 0.23906 | 0.25173 | 0.26442 | 0.27698 | 0.28961 | 0.30208 | 0.31458 | 0.32689 | 0.33925 | 0.35149 | 0.36375 | 0.37597 | 0.38823 | 0.4004 | 0.41268
 | 0.016545 | 0.029727 | 0.045647 | 0.061048 | 0.077277 | 0.095006 | 0.11354 | 0.13288 | 0.15274 | 0.17272 | 0.19259 | 0.21312 | 0.23333 | 0.25385 | 0.27448 | 0.29497 | 0.3156 | 0.33598 | 0.35675 | 0.37761 | 0.39841 | 0.4193 | 0.44015 | 0.46111 | 0.48214 | 0.50318 | 0.52416 | 0.54529 | 0.56632 | 0.58732
Business As Usual (BAU)
More Sustainable Development (MSD)
Impact fee for Low Impact Development non-compliance penalty:
  $13,000 per unit for single-family house
  $1,500 per unit for apartment home
Principal Agents: Prospective Homebuyer, Homeowners, Developers, Government
Implemented Policy Tool
After 30 years:
40% reduction in potable water demand from centralized plant in MSD as compared to BAU
36% increase in net property tax revenue generation in MSD as compared to BAU
Policy Implementation Effect
Source: Lu. et al., ES&T, 2013

## Slide 27: Integrated Simulation Models to Study Infrastructure Dependencies: Approach
Specification of common data model in SysML
Automated generation of federated simulations
Fast Runtime Infrastructure (RTI) software to interconnect models
Leverage industry standards, computational tools when available
System Specification
Integrated (Federated) Simulations
Cloud-Based Model execution
Visualization and Analysis
Common Object, Data Models, Simulations

## Slide 28
Spatial Databases for Urban Modeling
The SMARTRAQ project
Supports research on land use impact on transportation and air quality
1.3 million parcels in the 13 metropolitan Atlanta non-attainment counties

## Slide 29
SMARTRAQ Data and Attributes
Address
Road Type
City
Zip Code
Owner Occupied
Commercial/Residential
Zoning
Sale Price
Sale Date
Tax Value
Assessed Value
Improvement Value
Land Value
Year Built
No. of Stories
Bedrooms
Parking
Acreage
Land Use Type
Number of Units
X,Y Coordinate
Estimated Sq Feet
Total Sq Feet

## Slide 30: Projected Growth Scenarios for Atlanta
Business As Usual
Year 2030
More Compact Development
Year 2030

## Slide 31: ForeSEE: An Integrated Water-Energy-Cost Modeling Tool with Hourly, Daily, Monthly and Annual Forecasting
Hourly demand data used to project grid electricity and water savings from use of distributed water and energy technologies
Source: C. Golin and M. Cox (Credit: V. Thomas)
Notes: ForeSEE estimates of energy saved are determined by the productivity of solar panels during a specific hour during the average day and the peak day of a specific month coupled with the reduced energy required to distribute public water equal to the capacity that could be obtained on an average day. By 2020, the annual reduction in grid energy reaches 80,000 MWh, enough energy to avoid building three peaker gas-powered plants. Figure 2 shows the average hourly reduction in grid energy in 2020.

## Slide 32: Atlanta Water Demand for New Residential and Commercial Buildings in More Compact Growth Scenario (with low flow fixtures + decentralized CCHP system)
Installation of Air Cooled Microturbines save 2.4 times the amount of water used for domestic consumption

## Slide 33: Potential GHG and Cost Reductions in 2030
By 2030, implementation of CHP in all new residential and commercial buildings will reduce the CO2 emissions by~ 0.007 Gt CO2, NOx emissions by ~ 15000 Tons ,and the energy costs by $680 million per year for the Metro Atlanta region.
-25%
CO2 Emissions
NOX Emissions
Energy Cost
-23%
- 65%
-8%

## Slide 34: Summary
Infrastructure Systems Are All Connected and Greater Sustainability Gains Can be Achieved by Looking at Their Interactions
Decentralized Water / Low Impact Development Can Save Water, Energy and Money
Decentralized Energy and Combined Heat and Power Can Save Energy, Water and Money
Transportation and Land Use/ Planning Is Vital in Reducing the Impact Of Urban Systems and Examining Their Interactions
Complexity Models May Be Useful to Examine the Adoption Rate of Policy Instruments
Caveat: We need to test the ideas that were presented

## Slide 35: Emerging Engineering Solutions for Water and Human Sustainability
Water and Human Sustainability
Transit-oriented Development
Bike Friendly Neighborhood
Tele-commute to work
Shared Autonomous Vehicles
Network of Wireless Sensors
Social-Media Data Analytics
Understand Stakeholder Preference
Performance Monitoring
Network of Things
High Performance Buildings
Living Buildings
Energy Independent
Buildings
Grid Scale Energy Storage
Flow Batteries
Super Capacitors
Solar Powered Public transit
Decentralized Energy Infrastructure
Decentralized Water Infrastructure
Efficient Water Use

## Slide 36
Thank You!
John C Crittenden, Ph.D., P.E., U.S. and Chinese N.A.E.
E-Mail: john.crittenden@ce.gatech.edu
Zhongming Lu, Ph.D.
E-Mail: zhongming.lu@gatech.edu
Web Site: http://www.sustainable.gatech.edu/